## Slide 1
6 - 10 November 2023
Brisbane, Australia
Phindile Lydia Binda
A comparison of axle weight masses from a low-speed weigh-in-motion scale and a static weighbridge scale for the purpose of broadening law enforcement efforts

## Slide 2
WIM scale vs Static Weighbridge
Weigh-In-Motion uses in South Africa
Why Weigh-In-Motion is not used for law enforcement.
Why this study
Introduction/Background
Author
Phindile Binda
Notes: According to (Slavik, 2007), a WIM scale is "a technique for the measurement of axle loads without stopping vehicles" and "a scale that measures dynamic forces applied to the road surface by passing wheels."
Then vice versa, a static weighbridge scale is a scale that assesses

## Slide 3
Weigh-In-Motion History in South Africa (Slavik, 2007)
Permanent WIM Stations across South Africa(Kannemeyer, 2018)
Introduction
Author
Phindile Binda
Notes: Most of the WIM in SA are found along the Port Roads

## Slide 4
Data used comes from two 24 hours operating static weighbridge scales and 2 automated weigh-in-motion scales.
Methodology
Author
Phindile Binda

## Slide 5
Data used was from November 2022 to January 2023
Date, Time and Vehicle Registration numbers
Static weigh bridge data >> Weigh-In-Motion data
Data cleaning
Methodology
Author
Phindile Binda

## Slide 6
31 717 heavy Vehicles >> 26 vehicle configurations
3 744 >> 2 axle units, 9 585 >> 3 axle units, and 18 388 >> 4 axle units
2 axle units >> 3 Vehicle configurations
3 axle units >> 8 Vehicle configurations
4 axle units >> 15 Vehicle configurations
Methodology
Author
Phindile Binda

## Slide 7
All Vehicles Loading Status
Data Analysis & Results
Author
Phindile Binda
Total Number of Vehicles | Static Legal HV, s | Static Overload | Static Warning H
WIM Legal | 17 851(81%) | 230 (24%) | 3 966 (46%)
WIM Overload | 932 (4%) | 435 (46%) | 1 352 (16%)
WIM Warning | 3 269 (15%) | 280 (30%) | 3 402 (39%)
Total | 22 052 (100%) | 945 (100%) | 8 720 (100%)

## Slide 8
Axles which have an accuracy rate of 100% and +-15%.
𝐴𝑐𝑐(𝐴𝑐𝑐𝑢𝑟𝑎𝑐𝑦)=𝑊𝐼𝑀 𝑊𝑒𝑖𝑔ℎ𝑡𝑠/𝑆𝑡𝑎𝑡𝑖𝑐 𝑊𝑒𝑖𝑔ℎ𝑡𝑠∗100
Data Analysis & Results
Author
Phindile Binda
Axle. No | 85% <= Acc < 100% | Acc=100% | 100% < Acc <= 115% | Total Percentage
Axle1 | 42% | 8% | 46% | 96%
Axle2 | 21% | 7% | 63% | 91%
Axle3 | 36% | 8% | 36% | 80%
Axle4 | 21% | 5% | 26% | 52%
Notes: ASTM E 1318 (2002) ‘Standard Specification for Highway Weigh-In-Motion (WIM) Systems with User Requirements and Test Methods

## Slide 9
Data Analysis & Results
Author
Phindile Binda

## Slide 10
Axle Accuracy Rate of Legal Vehicles
Data Analysis & Results
Author
Phindile Binda
Axle No. | 85% <= Acc < 100% | Acc=100% | 100% < Acc <= 115% | Total Percentage
Axle1 | 41% | 8% | 45% | 94%
Axle2 | 21% | 7% | 65% | 93%
Axle3 | 35% | 8% | 36% | 79%
Axle4 | 24% | 6% | 29% | 59%

## Slide 11
Axle Accuracy Rate of Warning Vehicles
Data Analysis & Results
Author
Phindile Binda
Axle No. | 85% <= Acc < 100% | Acc=100% | 100% < Acc <= 115% | Total Percentage
Axle1 | 43% | 10% | 45% | 98%
Axle2 | 25% | 13% | 59% | 97%
Axle3 | 39% | 13% | 37% | 89%
Axle4 | 11% | 4% | 21% | 36%

## Slide 12
Axle Accuracy Rate of Overload Vehicles
Data Analysis & Results
Author
Phindile Binda
Axle No. | 85% <= Acc < 100% | Acc=100% | 100% < Acc <= 115% | Total Percentage
Axle1 | 43% | 7% | 48% | 98%
Axle2 | 31% | 9% | 56% | 96%
Axle3 | 25% | 6% | 21% | 52%
Axle4 | 4% | 1% | 11% | 16%

## Slide 13
Majority of the accuracy rates were among the +- 15%
Very few weights were 100% accurate.
WIM will always be a WIM
Future Work.
Discussion/Conclusion
Author
Phindile Binda