## Slide 1: ROAD FREIGHT ELECTRIFICATION AROUND THE WORLD USING ELECTRIC ROAD SYSTEMS
Parth Deshpande
Christopher de Saxe
Daniel Ainalis
John Miles
David Cebon
Centre for Sustainable Road Freight
Department of Engineering, University of Cambridge

## Slide 2: Road Freight Statistics
Authors:
P. Deshpande, C. de Saxe, D. Ainalis, J. Miles, D. Cebon
2
Source: OECD https://data.oecd.org/transport/freight-transport.htm
* EU data from major countries, i.e., France, Germany, Italy and Netherlands

## Slide 3: Electric Road Systems (ERS)
Authors:
P. Deshpande, C. de Saxe, D. Ainalis, J. Miles, D. Cebon
3
Image Credit: Dezeen.com
In-road (on-ground) power transfer
Wireless (inductive) power transfer
Overhead catenary cables
Image Credit: BusinessWire
Image Credit: Siemens Mobility GmbH

## Slide 4: Emissions Comparison
Authors:
P. Deshpande, C. de Saxe, D. Ainalis, J. Miles, D. Cebon
4
Source: 2020 Grid Electricity Emissions Factors v1.4 www.carbonfootprint.com | Emissions subject to change
Well-to-wheel efficiencies: 23% for FCEV, 70% for BEV, 77% for ERS EV
Diesel well-to-wheel efficiency: 38%; Emissions factor: 0.3 kg-CO2/kWh

## Slide 5: ERS Cost Breakeven Model
Authors:
P. Deshpande, C. de Saxe, D. Ainalis, J. Miles, D. Cebon
5
Construction time ()
98% usage ramp-up time ()
Breakeven point (at years)
Loan duration ()
Time (years)
Money in/out for maximum number of trucks () = 3000/day
Ref: Parth Deshpande et al. (2023), “A breakeven cost analysis framework for electric road systems”, Transportation Research Part D: Transport and Environment, ﻿103870.

## Slide 6: ERS Cost Breakeven Model
Authors:
P. Deshpande, C. de Saxe, D. Ainalis, J. Miles, D. Cebon
6

## Slide 7: ERS Cost Breakeven Results
7
Scenario | Description
(a) | Base case
(b) | Increased profit margin
(c) | Lower infrastructure costs
(d) | Longer loan duration

## Slide 8: ERS Cost Breakeven Results
Authors:
P. Deshpande, C. de Saxe, D. Ainalis, J. Miles, D. Cebon
8
India – ERS Cost: £1.8m / km
South Africa – ERS Cost: £1.8m / km
France – ERS Cost: £2m / km

## Slide 9: Journey Analysis Methodology
Authors:
P. Deshpande, C. de Saxe, D. Ainalis, J. Miles, D. Cebon
9
SRF Drive Cycle Synthesiser
Driver and Vehicle Model
Routing using
HERE Maps API
Adding stop locations as via points
Generating static charging signal
Generating ERS on/off signal
Driver behaviour
Vehicle systems:
Motor, inverter, transmission
Battery charging model
Energy consumption calculation
Origin and destination
Rest stop locations and durations
ERS locations
Drive cycle
Battery dip
Energy consumption
Ref: Christopher de Saxe et al. (2023), “An electric road system or big batteries: Implications for UK road freight”, Transportation Engineering, 100210.

## Slide 10: Case Study – Single Corridor (Canada)
Authors:
P. Deshpande, C. de Saxe, D. Ainalis, J. Miles, D. Cebon
10

## Slide 11: Case Study – Single Corridor (Canada)
11
Speed
Elevation
Battery dip
(static charging)
Battery dip
(ERS charging)
Battery dip
(no charging)
Static charging
(600 kW)
ERS charging
(150 kW)
Extra journey time due to charging stop
Drive Cycle
Battery Dip

## Slide 12: Case Study – Single Corridor (Canada)
Authors:
P. Deshpande, C. de Saxe, D. Ainalis, J. Miles, D. Cebon
12
Assumptions:
Tesla Semi – 36 tonnes gross, 12 tonnes tare (tractor), 4 tonnes (empty trailer)
Coefficient of drag: 0.36 (lower than most trucks)
Battery energy density: 0.186 kWh/kg
Battery size required = Lowest battery dip / 0.8
Battery dip
(static charging)
Battery dip
(ERS charging)
Battery dip
(no charging)
Static charging
(600 kW)
ERS charging
(150 kW)
Extra journey time due to charging stop
Battery Dip

## Slide 13: Case Study – Single Corridor (Canada)
Authors:
P. Deshpande, C. de Saxe, D. Ainalis, J. Miles, D. Cebon
13
Battery dip
(static charging)
Battery dip
(ERS charging)
Battery dip
(no charging)
Static charging
(600 kW)
ERS charging
(150 kW)
Extra journey time due to charging stop
Battery Dip
Charging Scenario | Required Battery Size (kWh) | Battery Weight (tonnes) | Max Payload (tonnes) | Journey Time (min)
No charging | 1538 | 8.2 | 16.3 | 596#
#similar to diesel HGV assuming no other stops.
*assuming an 850 kWh battery with the current charging strategy.
Static charging | 818 | 4.5* | 20* | 656
ERS charging | 325 | 1.4 | 22.8 | 596#

## Slide 14: Case Study – South Africa Long-Haul
Authors:
P. Deshpande, C. de Saxe, D. Ainalis, J. Miles, D. Cebon
14
Journey / Battery size (kWh) | No charging | ERS (a) | ERS (b) | SC | ERS (a) + SC | ERS (b) + SC | DC | ERS (a) + DC | ERS (b) + DC
Durban - Johannesburg - Pretoria | 1708 | 193 | 95 | 1138 | 193 | 95 | 1534 | 147 | 95
SC: static charging at rest stops, DC: static charging at drop locations.
Logistics company based in South Africa
Route: Durban to Pretoria via Johannesburg
Total distance: 675 km in 1 day
44 tonne HGV

## Slide 15: Case Study – South Africa Multi-Day
Authors:
P. Deshpande, C. de Saxe, D. Ainalis, J. Miles, D. Cebon
15
SC: static charging at rest stops.
Journey / Battery size (kWh) | No charging | ERS (a) | SC | ERS (a) + SC | ERS (b) | ERS (b) + SC
Day 1: Durban - Bethlehem | 1139 | 50 | 949 | 50 | 50 | 50
More off-ERS journeys: need large batteries, more charging stops or range extenders.
Day 2: Bethlehem - Worcester | 2116 | 20 | 1355 | 20 | 20 | 20
Day 3: Worcester - Port Elizabeth | 1476 | 1476 | 726 | 726 | 1476 | 726
Day 4: Port Elizabeth - Bloemfontein | 1589 | 1320 | 1209 | 942 | 1177 | 799
Max | 2116 | 1476 | 1355 | 942 | 1476 | 799

## Slide 16: Case Study – UK Multi-Drop Journeys
Authors:
P. Deshpande, C. de Saxe, D. Ainalis, J. Miles, D. Cebon
16
Journey | No charging | DC | ERS (a) | ERS (a) + DC | ERS (b) | ERS (b) + DC
(1) Aylesford - Eastbourne - Lewes - Marylebone - Aylesford | 818 | 336 | 456 | 223 | 413 | 223
SC: static charging at rest stops
DC: static charging at drop locations.
(2) Aylesford - Bloomsbury - Kensington Gardens - Ramsgate - Aylesford | 700 | 310 | 230 | 99 | 230 | 99
(3) Aylesford - Saxmundham - Woodbridge - Dover - Aylesford | 1152 | 466 | 475 | 226 | 172 | 79
Max | 1152 | 466 | 475 | 226 | 413 | 223

## Slide 17: Conclusions
Authors:
P. Deshpande, C. de Saxe, D. Ainalis, J. Miles, D. Cebon
17
ERS can electrify major freight routes in these countries with economic feasibility
Differences in countries in terms of geographic distribution of road freight and economics
Potential decarbonisation solutions: a mix of what is presented here
This analysis acts as a base for governments to promote Electric Road Systems
Evaluating battery swapping, pony express and range extenders
Modelling multiple journeys for determining optimal charging strategies
Future Work

## Slide 18: Thank You!
18
Parth Deshpande
prd41@cam.ac.uk | www.eng.cam.ac.uk/profiles/prd41
Centre for Sustainable Road Freight
Department of Engineering, University of Cambridge
www.csrf.ac.uk

## Slide 19: Appendix: ERS Cost Breakeven Model
Aim: To determine number of trucks required for cost breakeven
For 1 km of ERS:
  Expenditure:
    Infrastructure (£2m) on loan
    Maintenance (5%)
  Profit:
    Electricity selling (7p/kWh) - Depends on number of trucks
Authors:
P. Deshpande, C. de Saxe, D. Ainalis, J. Miles, D. Cebon
19
Capital cost of ERS (£/km)
Number of years for breakeven
Annual maintenance cost fraction
Sum of inflation terms over years
Number of days of ERS use per year
Energy transferred per vehicle (kWh/km)
(= Max. power / average speed)
Electricity profit margin (pence/kWh)
Maximum number of trucks
Annual loan instalment fraction
Ramp-up curve for number of trucks using the ERS
Number of years for ERS construction
Number of years for 98% ERS usage
^ In terms of freight flow
Annual freight flow (t/year)
Energy efficiency of freight (kWh/t-km)
Number of days of ERS usage (days/year)
Max. number of trucks (1/day)
Energy transferred per vehicle (kWh/km)
Ref: Parth Deshpande et al. (2023), “A breakeven cost analysis framework for electric road systems”, Transportation Research Part D: Transport and Environment, ﻿103870.