## Slide 1: PERFORMANCE ANALYSIS OF AN A-DOUBLE IN ROUNDABOUTS USING NATURALISTIC DRIVING DATA
Abhijeet Behera
Sogol Kharrazi
Erik Frisk

## Slide 2: Introduction
Abhijeet Behera, Sogol Kharrazi, Erik Frisk
PERFORMANCE ANALYSIS OF AN A-DOUBLE IN ROUNDABOUTS USING NATURALISTIC DRIVING DATA
Data collected unobtrusively in real-traffic (uncontrolled environment)
  Performance-based standards (PBS)
  Tracking
    Low-Speed Swept Path
    Tail Swing
32 m

## Slide 3: Motivation and Research Questions
Abhijeet Behera, Sogol Kharrazi, Erik Frisk
How much space (Tracking) do A-doubles occupy in the roundabouts?
How do drivers respond to roundabouts?
[1] https://www.youtube.com/watch?v=gYVnp9x6UCk
2.7x
Test by Volvo Trucks [1]

## Slide 4: Research Objectives
Abhijeet Behera, Sogol Kharrazi, Erik Frisk
Estimate the influence of the roundabout’s radius on the Low-Speed Swept Path (LSSP) and Tail Swing (TS).
Analyze the steering and speed patterns of drivers of A-doubles in the roundabouts.
Evaluate the cognitive workload of the drivers of A-doubles in the roundabouts using Steering Reversal Rate (SRR).

## Slide 5: Data Collection
Abhijeet Behera, Sogol Kharrazi, Erik Frisk
Gothenburg
Malmö
Piteå
OxTS RT3000
Differential GPS and IMU
Accuracy of 1 cm under clear sky
Positions, translational and angular velocities, and corresponding accelerations
Fixed in first and last units
540 km, 6 trips
40 km, 35 trips

## Slide 6: Roundabout Categorization
Abhijeet Behera, Sogol Kharrazi, Erik Frisk
9 Roundabouts: 152 Crossings
Direction of travel | No. of cases
Straight | 130
Left | 11
Right | 11
Radius of roundabouts | No. of cases
R11 | 22
R15 | 17
R24 | 21
R30 | 92

## Slide 7: Steering Angle and Speed (1)
Abhijeet Behera, Sogol Kharrazi, Erik Frisk
Ring
Ring
Ring

## Slide 8: Steering Angle and Speed (2)
Abhijeet Behera, Sogol Kharrazi, Erik Frisk
  Exit speed is around 2 times the entry speed.
  Entry and exit speeds increase with the radius of the roundabout.

## Slide 9: Workload: Steering Reversal Rate
Abhijeet Behera, Sogol Kharrazi, Erik Frisk
Steering Reversal Rate (SRR) is the number, per minute, of steering wheel reversals larger than a certain minimum angular value [2].
[2] Markkula G, Engström J. A steering wheel reversal rate metric for assessing effects of visual and cognitive secondary task load. In Proceedings of the 13th ITS World Congress 2006. Leeds.
SRR

## Slide 10: Workload: Steering Reversal Rate
Abhijeet Behera, Sogol Kharrazi, Erik Frisk
Cognitive workload decreases with the radius.
The right turns are more workload-intensive than straight crossings.

## Slide 11: Swept Path
Abhijeet Behera, Sogol Kharrazi, Erik Frisk
Low-Speed Swept Path (LSSP) is the maximum width of the swept path, i.e., the maximum road width swept out by the extremities of the vehicle as it moves along the path.

## Slide 12: Swept Width Variation
Abhijeet Behera, Sogol Kharrazi, Erik Frisk
Three peaks for straight and left turns in the roundabout compared to one peak in right turn.
The magnitude of the peak is mostly the highest in the ring. (It may not be always true!)

## Slide 13: Low-Speed Swept Path (LSSP)
Abhijeet Behera, Sogol Kharrazi, Erik Frisk
Straight
Left
Right
  LSSP decreases with instantaneous radius irrespective of the roundabout’s radius for straight and left.
  Large variance in instantaneous radius (also LSSP) for smaller radii compared to higher radii for straight.
  Small variance in instantaneous radius (also LSSP) for left cases.

## Slide 14: Conclusions
Abhijeet Behera, Sogol Kharrazi, Erik Frisk
The A-double needs steerable axles to satisfy the existing LSSP requirement for 25.25 m combinations in Sweden (12.5/2.0 m of outer/inner radius).
A-doubles are driven safely in all the studied roundabout crossings.

## Slide 15: Acknowledgement
Abhijeet Behera, Sogol Kharrazi, Erik Frisk
Funding Agency
Data Collection

## Slide 16: Thank you for listening! 
Abhijeet Behera, Sogol Kharrazi, Erik Frisk