## Slide 1: Introducing a Novel Method for Measuring Rolling Resistance and Dynamic Vertical Load on a Semi-Trailer Suspension
William Levesque, CPI, Ph.D. Candidate
André Bégin-Drolet, ing., Ph.D.
Julien Lépine, ing., Ph.D.

## Slide 2: Research Project with the Quebec Ministry of Transport and Sustainable Mobility
William Levesque, André Bégin-Drolet, Julien Lépine
Pavement types (i.e. Flexible vs Rigid) and fuel consumption comparison
Consideration for cold climate conditions
Many on-road physical phenomena to consider

## Slide 3: On-road experimental approaches
William Levesque, André Bégin-Drolet, Julien Lépine
Many disturbing factors
No normalized conditions
Need for a more direct approach for rolling resistance measurements

## Slide 4: Novel Method of Measurement
William Levesque, André Bégin-Drolet, Julien Lépine
Measuring all forces and movements between the suspension and the semi-trailer frame
No major modifications
Direct computation of dissipated energy in the damper
  Road Roughness

## Slide 5: Conceptual Approach
William Levesque, André Bégin-Drolet, Julien Lépine
Solving the equations of the free-body diagram
Consideration for :
  Damping force
  Dynamic vertical load
  Road slope
  Vehicle acceleration
Four-bar mechanism and kinematic model

## Slide 6: Installation of custom-made sensors
William Levesque, André Bégin-Drolet, Julien Lépine
Bolted assembly welded on each frame bracket
  Four in total
Measure forces in two orthogonal directions

## Slide 7: Load Cell Design and Laboratory Calibration
William Levesque, André Bégin-Drolet, Julien Lépine
Dynamic forces to measure (i.e. 2kN)
  Expected maximum rolling resistance of ≈0.2kN (per load cell)
Brakes installed on the suspension
  Force up to 20kN (per load cell)
  Mechanical end-stop

## Slide 8: Other measurement systems [1]
William Levesque, André Bégin-Drolet, Julien Lépine
Damping force
  Load pin
Damper displacement
  Linear potentiometer
Air bellow weight
  Low-profile load cell

## Slide 9: Other measurement systems [2]
William Levesque, André Bégin-Drolet, Julien Lépine
TTPMS at the center of the rim
  Internal temperature at 16 points
  Inflation pressure
  Installed on each side of the axle
MEMS
  Pitch angle
  Vehicle acceleration
GPS
Custom-made data-acquisition system

## Slide 10: Experimental Campain
William Levesque, André Bégin-Drolet, Julien Lépine
During September and October 2023
Focus on highway conditions at constant speed (i.e. 95 km/h)
Measurements on various pavements
  Rigid vs Flexible
Generally a straight and flat road
  Low average pitch angle (< 0.05 degree)
  Low maximum pitch angles (< 1.5 degree)
Tire temperature stabilization

## Slide 11: Preliminary Results: Right Frame Bracket Longitudinal Force
William Levesque, André Bégin-Drolet, Julien Lépine
Physical aspect to consider:
  Road slope
  Vehicle acceleration
  Damping force
  Suspension aerodynamics
Estimated
  Rigid: 6.0 kg/ton
  Flexible: 6.8 kg/ton
Difference: 22N

## Slide 12: Conclusion
William Levesque, André Bégin-Drolet, Julien Lépine
Successfully installed and used on real roads
More data analysis is required:
  Implementation of the whole model
  Tire vibration
  In-depth comparision Rigid vs Flexible
Validation of the instruments
Experimental is hard (but worth it)