## Slide 1: Decarbonising the UK’s heavy goods vehicles: Lessons from the UK for Australia
Dr Daniel Ainalis1,2
Dr Christopher de Saxe2
Prof. David Cebon2
1 Sustainability and Materials Performance, National Transport Research Organisation 2 Centre for Sustainable Road Freight, Department of Engineering, University of Cambridge
Daniel.Ainalis@ntro.org.au
Prof. John Miles2

## Slide 2: Presentation outline
Context.
Developments in decarbonising UK Heavy Goods Vehicles (HGVs).
What can Australia learn from the UK?
Summary and next steps.
Authors:
Daniel Ainalis, Christopher de Saxe, John Miles, and David Cebon

## Slide 3: Context
UK mandate for net zero emissions by 2050.
Transport is largest emitting UK sector.
HGVs: outsized emissions (5% UK total).
Authors:
Daniel Ainalis, Christopher de Saxe, John Miles, and David Cebon
Chart: 
| Passenger Cars | Light Duty Vehicles | Buses | HGVs | Motorcycles
 | 0.60929 | 0.17012 | 0.029324 | 0.18156 | 0.004643
UK GHG emissions by transport mode (2017)

## Slide 4: Pathways for zero emission HGVs in the UK
Authors:
Daniel Ainalis, Christopher de Saxe, John Miles, and David Cebon
Biofuels
Tailpipe emissions.
Fuel stations.
Source of fuels?
Battery Electric
Zero tailpipe emissions.
Large on-board battery.
Slow/fast chargers.
Battery Electric with Electric Road System
Zero tailpipe emissions.
Small on-board battery.
Dynamic (on-the-go) charging.
Hydrogen Fuel Cell
Zero tailpipe emissions.
Hydrogen fuel stations.
Hydrogen production?

## Slide 5: Overview of UK progress and developments
UK Government
Feasibility studies across 3 streams to support decarbonisations of HGVs (£20mn).
Real-world demonstration programme (£200mn).
Phase out dates for sale of new non-zero emission HGVs:
  2035 for HGVs less than 26 t.
  2040 for all HGVs.
Authors:
Daniel Ainalis, Christopher de Saxe, John Miles, and David Cebon
*Decarbonising the UK’s Long-Haul Road Freight at Minimum Economic Cost: http://bit.ly/csrfwhitepaper
CSRF Research
Roadmapping: decarbonisation of road freight only possible by electrification.
Several studies on electrification of road freight and HGVs, including white paper*.
Electric Road System (ERS) most promising.
ERS national feasibility study.

## Slide 6: Electric road system for heavy goods vehicles
Authors:
Daniel Ainalis, Christopher de Saxe, John Miles, and David Cebon
Poles and arms to support catenary
Pantograph system
Catenary wires
On-the-move charging: power vehicle & charge battery.
Smaller battery, highest efficiency.
Reduces stationary charging power and infrastructure.
Significant infrastructure building: high upfront costs to install.

## Slide 7: UK electric road system feasibility study: Overview of project
£2 million (£1.2 million funded).
July 2021 – March 2022.
Aims:
UK demonstrator plan and costings.
Understand the reality of UK logistics.
Optimal dynamic charging vs static charging vs battery size.
National transition models (economic and environmental).
Authors:
Daniel Ainalis, Christopher de Saxe, John Miles, and David Cebon
Consortium

## Slide 8: UK electric road system feasibility study: Proposed demonstrator programme
Authors:
Daniel Ainalis, Christopher de Saxe, John Miles, and David Cebon
Doncaster
Immingham
M180
ERS
Grimsby
to Sheffield, Manchester, South
to Leeds, Manchester, North
to Europe
Minimum 30 lane-km
= 15 km in both directions
~80 km

## Slide 9: UK electric road system feasibility study: National network topologies
Authors:
Daniel Ainalis, Christopher de Saxe, John Miles, and David Cebon
2,750 km
5,500 km
8,500 km
Length (2-way):

## Slide 10: UK electric road system feasibility study: Trade-offs in static and dynamic charging
Authors:
Daniel Ainalis, Christopher de Saxe, John Miles, and David Cebon
Chart: Average battery size reduction [%]
| ERS Lite | ERS Medium | ERS Heavy
None | 0.43 | 0.64 | 0.79
Drop-Off | 0.38 | 0.58 | 0.71
Rest Stops | 0.42 | 0.64 | 0.74
No static charging
43%
79%
64%
Drop-off charging
38%
71%
58%
Rest stop charging
42%
74%
64%

## Slide 11: UK electric road system feasibility study: National economic modelling
Authors:
Daniel Ainalis, Christopher de Saxe, John Miles, and David Cebon
Chart: Total Government Cost [£bn]
| Green H2 FCEVs | ERS Light (500 kWh) | ERS Light (300 kWh) | ERS Light (150 kWh)
 | 14.2944 | 19.809 | 15.4794 | 11.4558
 | 34.4749 | 5.631 | 5.631 | 5.631
ERS construction costs, ERS utilisation, average fleet battery size, and electricity price
Wholesale electricity price and technology for green H2 production and transport

## Slide 12: What can Australia learn from the UK?
Can we take the UK approach and apply it in Australia?
Differences to UK:
  Geography (range and operational requirements).
  Longer and heavier vehicle combinations.
  Performance-based standards.
  Emissions standards (lack of).
Authors:
Daniel Ainalis, Christopher de Saxe, John Miles, and David Cebon
Credit: Norman Patrick Trickey Blake

## Slide 13: What can Australia learn from the UK?
Zero emission road freight
Authors:
Daniel Ainalis, Christopher de Saxe, John Miles, and David Cebon
Industry associations
Government and regulators
Research and academic organisations
Freight buyers and shippers
Freight companies (operators)
Vehicles
Infrastructure
Digital and data
Energy, grid operators, utilities
Funders and financing
Site owners and developers
Performance-based standards
National telematics framework

## Slide 14: What can Australia learn from the UK?
Authors:
Daniel Ainalis, Christopher de Saxe, John Miles, and David Cebon
Study
Deploy
NOW
2050
Demo
Nationally-consistent real-world assessment of solutions
Wide stakeholder groups
Independent evaluation for robust evidence base
Wide-dissemination
Kick-start initial infrastructure and signal demand to OEMs
Coordinated long term planning and investment
National alignment
Emissions targets and phase out dates
Large body of knowledge exists
Identify gaps/ differences to Australian context
Identify potential alt. solutions
Define feasible future pathways

## Slide 15: Decarbonising the UK’s heavy goods vehicles: Lessons from the UK for Australia
Dr Daniel Ainalis1,2
Dr Christopher de Saxe2
Prof. David Cebon2
1 Sustainability and Materials Performance, National Transport Research Organisation 2 Centre for Sustainable Road Freight, Department of Engineering, University of Cambridge
Daniel.Ainalis@ntro.org.au
Prof. John Miles2